## Slide 1: Building community resilience to flooding
Tom Shopland
Natural Flood Management Advisor
Tom.Shopland@fwagsw.org.uk

## Slide 2
2014 Somerset 20 Year Flood Action Plan
Dredging and River Management – EA
Urban Run-off – District Councils
Resilient Highways Infrastructure – Highways Authority
Building Local Resilience – District Councils
Major Infrastructure Schemes – EA
Somerset Rivers Authority – County Council/IDB
Land Management – FWAGSW

## Slide 4
HEAVY RAIN
Volume
Reduced flood water volume through successful Natural Flood Management
Flood peak without interventions
Flood peak with NFM interventions
Time
“Every farm, every field and every stream has a part to play”
Natural Flood Management

## Slide 5
In field
Edge of field
In stream
Reduce the occurrence of run-off and erosion within fields. Encourage rainwater infiltration into the soil by good soil management practices.
Intercept, slow, divert flow pathways before soil and water leave the field
Further slow the water and trap sediment in receiving ditches and streams. Reconnect streams with their flood plains the floodplain

## Slide 6: In field
Strategic tree planting
And hedges
Soils and land
management advice

## Slide 7: Edge of Field
Bund & hedge
Buffer strips
Ponds & wetlands

## Slide 8: In Stream
Leaky dams
Renaturalising
watercourses
Online ponds

## Slide 9
NFM Interventions 2015-2024

## Slide 10
NFM Interventions 2015-2024
386 sites/farms – some with multiple interventions | Number of Interventions | 
In-stream (leaky dams, check dams, flow spreaders) | 333 | 
In-field (filter fences, filter sox, coir rolls) | 121 | 
Water storage (leaky ponds, scrapes, floodplain storage, bunds) | 146 | 
Strategic planting (trees and hedges) | 71 | 
Infrastructure (e.g. cross drains, fencing, yard improvements) | 85 | 
TOTAL | 756 | 
Land Management sites | 93 | 
Soil husbandry | 3429ha | 

## Slide 11
In field
Where to start?
2. Collecting local knowledge
Create a central space to gather information
Where are the flooding hotspots?
Walk/photograph the land on wet days
1. Form a community action group
What geographic area will your project cover?
Who can help: parish council, residents, farmers, landowners, agencies, organisations
How are other communities building resilience?
3. Identifying interventions
Where would an intervention most help?
Are there landowners and farmers who can help?
Get quotes from earthworks/drainage contractors

## Slide 12
What are the next steps?
Who else should we speak with?
Where would an intervention have the most impact?
Who can do what?